## Slide 1: Digital Terrain Model Generation from GPS Point Cloud
Shuai He, Conan Jennings

## Slide 2: What is a Digital Terrain Model (DTM)?
Digital Terrain Model
  Contains only terrain features
Digital Surface Model
  Contains surface heights
Digital Elevation Model
  Often synonymous with DTM
  Elevation rendering

## Slide 3: Applications of HD DTM/DEM
Flight planning and simulation
3D modeling for aerial/satellite photography
Engineering and Infrastructure design
Precision farming and forestry
Intelligent transportation system

## Slide 4: DTM Data Collection
Data collected from various sources
  Spot Heights (xyz)
  Stereo Images
  Radar
  Lidar

## Slide 5: Approaches
Grid Structure
Record elevation at each node
Interpolate smooth surface between grid points
Appears more natural
Redundant Data
TIN (Triangulated Irregular Network)
Record X, Y, Z at surface point
Interpolate triangular surface between points
Unnatural representation of terrain

## Slide 6: Grid vs TIN

## Slide 7: Preprocessing Point Cloud
.fuse – lon, lat, alt, intensity
Lla -> ECEF (Earth-centered, earth-fixed)
ECEF -> NED (North East Down)

## Slide 8: Results (grid)

## Slide 9: Results (TIN)

## Slide 10: Finalized Method
Use the grid approach for querying points and collecting data
Filter data based on neighbors to limit space complexity of data structure
Natural render while preserving space

## Slide 11: Future
More accurate conversion for local point cloud data
Better boundary definition and filtering method

## Slide 12: Sources
Ma, Ruijin. "DEM generation and building detection from lidar data." Photogrammetric Engineering & Remote Sensing 71.7 (2005): 847-854.
Yunfei, Bao, et al. "Classification of LIDAR point cloud and generation of DTM from LIDAR height and intensity data in forested area." The International Archives of the Photogrammetry, Remote Sensing and Spatial Information Sciences 37.7 (2008): 313-318.
"NCGIA CCTP Unit 6." NCGIA CCTP Unit 6. N.p., n.d. Web. 07 Mar. 2017.